## Slide 1: VP_A380 Platform Quick Start
PBS

## Slide 2: Agenda
A380 Hardware
VP_A380 EVB and Jumper Setting (FEVB_IP_FIE3380_VIRTUAL_PLATFORM_A380)
VP_A380 Software Package
Recommended Debug Tools
Booting Sequence
Quick Start with Linux OS

## Slide 3: VP_A380 Hardware

## Slide 4: A380 Overview
Processors
  Dual-core ARM Cortex-A9
  FA626TE
External memories supported
  DDR3, SRAM, NAND/NOR Flash
  SDHC/SDXC card
Connectivity
  USB2.0 (host, OTG) with PHYs
  SGMII, PCIe G2, SPI, I2S, I2C and UARTs
Peripherals & FPGA connections
  AHB extension bus
Process
  UMC 40nm LP

## Slide 5: A380 Block Diagram

## Slide 6: VP_A380 EVB and Jumper Setting

## Slide 7: VP_A380 EVB Top View
DC 5V input
Micro SD Card Socket
UART Console
Gigabit Ethernet
Power Switch
FAS626 ICE Port
Boot Mode &
PLL Setting
CPU &
PLL Setting
AHB HCLK
Skew Setting
CA9 ICE Port
D-SUB connector

## Slide 8: VP_A380 CA9 Jumper Setting
CPU select:
  CPU_SEL[1:0] = 2’b00
Clock Setting (PLL4 jumper)
  PLL4_NS[2:0] = 3’b000

## Slide 9: VP_A380 Boot mode Setting
Use Manual mode
{J48, J47, J46} = Boot_mode[2:0] = 3’b110

## Slide 10: VP_A380 Software Package

## Slide 11: Software Package Contents
  Document
  A380 Hardware datasheet
  FIE3380 Linux User Guide
  FIE3380_VP_EVB User Guide
Software Packages
  CVD script & SPL
    VP_A380.cmm
    Boot.bin
  Toolchain
    arm-linux-gnueabi-gcc (Ubuntu/Linaro 7.5.0-3ubuntu1~18.04) 7.5.0
  U-boot source code
    U-boot.tar.gz
  Linux source code
    Linux.tar.gz
  Images(Prebuilt mages)
    Bootloader/u-boot/zImage_dtb

## Slide 12: Recommended Debug Tools

## Slide 13: Recommended ICE and Debugger
Debugger : ARM DS
ICE : ARM D-Stream
(http://ds.arm.com)
Debugger : JnD CVD
ICE : CodeViser
(http://jndtech.com/main/)
Recommended: Use JnD CVD ICE

## Slide 14: Booting Sequence

## Slide 15: VP_A380’s Booting Sequence
emROM Code
(IPL)
Boot mode
: From ICE
nonos
u-boot
zImage
SPL
DDR init
3’b110
Booting Mode Setting
J48,47,46
OS
VP_A380.cmm

## Slide 16: Quick Start with Linux OS

## Slide 17: Getting Started Guide with Linux OS
Refer to FIE3380_Linux_User_Guide.pdf

## Slide 18: Pre-Work for Running Linux
USB-to-Serial Cable
DC-5V Power Adapter
ICE for CA9
USB miniA to StdA
USB pen drive
②
①
③
④
⑤

## Slide 19: How to Compile U-boot
Install GCC tool chain
  Install from Ubuntu 18.04:
    # sudo apt update
    # sudo apt install gcc-arm-linux-gnueabi
Compilation procedures
  Step1: Unpack the file “U-boot.tar.gz”
  Step2: Build code
    # make a380_defconfig;make CROSS_COMPILE=arm-linux-gnueabi-
    U-boot.bin Image will be placed at “$TOP_DIR/”

## Slide 20: How to Compile Linux (1/2)
Install GCC tool chain
  Install from Ubuntu 18.04:
    # sudo apt update
    # sudo apt install gcc-arm-linux-gnueabi
Compilation procedures
  Step1(just run once): Load the default CPU/memory/IP test settings
    # make a380_defconfig
  Step2: Customize the test items by using the configuration system
    # make menuconfig

## Slide 21: How to Compile Linux (1/2)
Compilation procedures
  Step3(just run once): Add Ram disk Path to kernel
    Untar the rootfs.gz to some folder
    # make menuconfig
    Enter General setup
    Enter filesystem path
  Step4: Build code
    # make a380_defconfig;make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi-
    # cat arch/arm/boot/zImage arch/arm/boot/dts/faraday-a380.dtb> zImage_dtb
    Linux zImage_dtb will be placed at “$TOP_DIR/arch/arm/boot”

## Slide 22: Run Linux – Using ICE Script to Load Linux Image
Step1 : Serial Port parameter setting
on your computer
Step2: Turn on the VP_A380 EVB power,
you will see right screen, please don’t
chose any number.
Step3 : Execute CVD IDE(Depend on debugger tool used)

## Slide 23: Run Linux – CVD usage
Step4 : Open “Run Script File” and program will be executed
  VP_A380.cmm is placed in ICE_script\
Step5: Start to download U-boot & Linux Image
After downloading Linux Image, U-boot is running
  See next page
Note : Before run script file, please modify image path in the script file : zImage_dtb,u-boot.bin,boot.bin

## Slide 24: U-boot booting
Step6: Enter go command to boot Linux
  # go 0x43000000

## Slide 25: Linux Booting

## Slide 26: USB Disk mounting

## Slide 27
Confidential information
  The material is being disclosed to you pursuant to a non-disclosure agreement between you or your employer and Faraday. Information disclosed in this presentation may be used only as permitted under such an agreement.
Legal notice
  The information contained in this presentation is intended to provide a general guide as to which product is suited for a given requirement and shows suggested product applications. Specified functions and properties for products are only valid when handling instructions and other stated conditions and recommendations have been considered and followed. All descriptions, illustrations and dimensions in the information represent general particulars and do not form part of any contract. All information is provided “as is”, with no guarantee of completeness, accuracy, timeliness or of the results obtained from the use of the information, and without warranty of any kind, express or implied, including but not limited to warranties of performance. All information is subject to change without prior notice. Faraday assumes no responsibility whatsoever for any errors or inaccuracies about the information.